## Slide 1
01
Two real boards in a simulated fleet
HITL ARCHITECTURE
Each aircraft runs in its own Linux network namespace with a real IP stack. One Ethernet cable per board carries two tagged VLANs, so the camera feed and the radio link share a wire but are different networks — and only one is degraded.
VLAN 10 · sensor · unimpaired
VLAN 42/43 · radio · through ns-3
HOST — UBUNTU 22.04 / ROS 2 HUMBLE
Gazebo · physics + 2 cameras
640×384 · 5 Hz · 45° down
0.6 rad FOV · small_city world
netns uav1ns · ArduPilot SITL
10.42.0.11 · sysid 1 · AP_DDS
netns uav2ns · ArduPilot SITL
10.42.0.13 · sysid 2 · AP_DDS
netns gcsns · ground station
drone_bridge ×2 — commands out
micro_ros_agent ×2 — telemetry in
gcs_receiver ×2 — detections in
10.42.0.10
ns-3 · simulated radio
three_uav_tapbridge_integrated
TapBridge injects the channel
model into real Linux packets
802.11 · Nakagami fading
nodes 0–3 · GCS + UAVs + edge
Detections cross HERE.
Camera frames never do.
EDGE NODES
Raspberry Pi 4B — UAV1 edge node
YOLO11n · OpenVINO FP32 · 384×640
conf 0.40 · class 0 (person)
cam 10.0.0.2 · radio 10.42.0.12
measured: 337 ms · 2.85 fps
Raspberry Pi 4B — UAV2 edge node
YOLO11n · OpenVINO FP32 · 384×640
conf 0.40 · class 0 (person)
cam 10.0.1.2 · radio 10.42.0.14
measured: 240 ms · 4.01 fps
camera frames · 737 KB/frame
detections · 73–504 B JSON
ISOLATION IS REAL, NOT SIMULATED
Network namespaces give each aircraft a genuine kernel stack — separate routing tables and its own 127.0.0.1. Nothing shortcuts through loopback, so the packets ns-3 degrades are the packets the flight code sent.
ONE CABLE, TWO NETWORKS
802.1Q VLAN tagging splits each board's link. VLAN 10 behaves like a camera ribbon; VLAN 42/43 is bridged into ns-3 — modelling an airframe where sensor bus and radio are separate systems.
ONLY RESULTS CROSS THE RADIO
A 737 KB frame stays on the sensor link. What crosses the degraded channel is 73–504 bytes of JSON. That reduction is the architectural claim edge processing makes, and what this experiment measures.

## Slide 2
02
Human detection on the airframe
EDGE INFERENCE
Each board subscribes to its own aircraft's camera, runs YOLO11n under OpenVINO, and publishes only the bounding boxes. Whether a person is detectable at all is set by six physical and software parameters, derived and measured below.
GROUND
UAV
30 m
blind: 0–20.6 m
20.6 m
43.6 m
visible band
≈30 px
45° pitch · 0.6 rad
640×384 @ 5 Hz
band = 0.687h
… 1.453h
GSD & pixel-height derivation → parameters 1 and 3, right
DETECTION SENSITIVITY PARAMETERS
1 Ground Sampling Distance (GSD)
GSD = 2h*tan(HFOV/2)/W = 2.9 cm/px @ 30 m (nadir-equiv)
2 Camera resolution
640x384 px, frozen by the OpenVINO export shape
3 Person height in pixels
px = 889 / altitude(m) -> 30 px @ 30 m, 45 px @ 20 m
4 Altitude
drives GSD & pixel height directly; reliable window ~15-25 m
5 Flight speed -> motion blur
blur(px) = v x t_exposure / GSD -- not modeled by Gazebo's camera
6 Gimbal pitch
pixel height peaks at 45 deg; steeper widens the COCO->aerial gap
7 Inference backend (measured)
OpenVINO 236 ms < NCNN 270 < MNN 342 < PyTorch 1,027 (PI_SETUP.md)
8 Confidence vs IoU
conf 0.40 explicit vs IoU 0.70 (NMS default) -- different filters
WHAT THIS MEANS FOR THIS DEPLOYMENT
Frames are dropped by design: BEST_EFFORT, KEEP_LAST, depth 1 means the detector always works the newest frame instead of a queue, so discarded frames were never processable anyway. Geometry, not the model, sets the ceiling — camera resolution is frozen at the export shape, so a person's pixel height is fixed by altitude and pitch alone once conf and IoU are set.
MEASURED CONSEQUENCE
UAV1 held station near a static group: 50 of 357 frames detected a person (14.0 %).
UAV2 overflew the walking subject at the same altitude and settings: 8 of 523 (1.5 %).
Same model, same conf/IoU, same boards. The gap is dwell time on target — exactly what parameters 3-6 above predict.

## Slide 3
03
Output, and how it was validated
OUTPUT & VALIDATION
One instrumented mission, both boards. Every figure below is read from the run's own logs by scripts/summarise_run.sh — no hand-copied numbers.
96 % / 96 %
OF COMPUTE CEILING
2.85 and 4.01 fps against limits of 2.97 and 4.17
337 / 240 ms
MEAN INFERENCE
board 1 ranged 244–797, board 2 213–485
97.2 % / 87.0 %
DELIVERED ACROSS ns-3
347/357 and 455/523 detection messages reached the GCS
104 / 76 B
MEAN PAYLOAD
73 B empty result, up to 504 B with several people
HOW A RUN IS VALIDATED
STEP 0
rpi_init.sh
16 checks per board: link, VLAN addressing, RTT, socket buffers, clock skew ≤ 50 ms
STEP 1
sitl_init.sh
Cold-starts netns, ns-3, Gazebo, SITL. Waits for a real navsat message per aircraft
STEP 2
detector_start.sh
Starts both edge detectors, blocks until each reports its model loaded
STEP 3
run_missions.sh
Re-checks every stage before arming, flies, then archives and summarises the run
WHAT THE INSTRUMENTATION REVEALED
Board 1 is power-limited, not heat-limited.
It ran hotter work more slowly (337 ms) than board 2 (240 ms) while staying cooler — 66.2 °C peak against 72.0 °C. Its throttle flag reads 0x50000: under-voltage, not temperature. A better supply, not a heatsink.
Both boards ran at 96 % of their own compute ceiling.
Delivery was never the constraint: if the link were starving them, the achieved rate would sit well below what inference allows. It does not.
Board 2 lost 13 % of its detections crossing ns-3.
455 of 523 arrived, against 97.2 % on board 1 — a real difference between the two radio links, not measurement noise.
STATED LIMITATIONS
INT8 quantisation was evaluated and rejected.
The quantised model was verified correct on x86, but OpenVINO's ARM CPU plugin could not compile the graph on the Pi 4B. Edge inference runs FP32.
Board power is not instrumented.
The Pi 4B exposes no power sensor. ARM clock, core voltage and CPU load are logged as on-board proxies; absolute wattage needs an inline meter.
Throttling changes timing, never accuracy.
A throttled CPU produces bit-identical detections more slowly. It reduces frames analysed per target pass — not precision or recall.
Source: results/20260903_163917 · 357 + 523 frames · 125 s and 130 s of flight · FP32 YOLO11n